Inertial Management Unit (IMU)
Algorithm Description Document (ADD)

by
Simeon Symeonidis

02/20/2015
revision 1.0

Overview

The purpose of the IMU is to translate Microelectromechanical Systems (MEMS) accelerometer, magnetometer, and gyroscope sensor data into orientation and acceleration measurements.

The algorithm assumes synchronous data. In cases where sensors operate at different rates, it is necessary to interpolate the data into a common reference frame. MI software interpolates lower rate magnetometer and accelerometer data to gyroscope data using timestamps. Other state estimation approaches could eliminate this need to synchronize data, but at the cost of design complexity and measurement bandwidth, i.e. Kalman Filters often reduces near-Nyquist signals. This trade should be re-investigated if there arises a need for a low-latency solution.

The work captured hereinafter is an extension of the paper “An efficient orientation Filter for inertial and inertial/magnetic sensor arrays” written by Sebastian O.H. Madgwick. The algorithm was adapted to meet the needs of a human wearable sensor operating in the presence of Electromagnetic noise.

The report will be organized in three sections. The first section defines variable types and operations to be used in the IMU. This is important because it will establish the conventions to be used within the paper. The second section defines algorithm inputs and outputs. The last section documents the actual algorithm.

Definitions

Sensor inputs will be represented as three dimensional vectors, denoted lowercase letter with an arrow on top. Common vector operations, normalize, dot products and cross products, are captured below.

vec v = left[matrix{v_1##v_2##v_3} right] abs {vec x} = sqrt{{x_1}^2+{x_2}^2+{x_3}^2} hat{x} = left[ matrix {x_1/ abs{vec x} ##x_2/abs{vec x}##x_3/abs{vec x}} right] vec x cdot vec y = x_1 cdot y_1 + x_2 cdot y_2 + x_3 cdot y_3 vec x times vec y = left[matrix{x_2 y_3-x_3 y_2##x_3 y_1-x_1 y_3##x_1 y_2-x_2 y_1} right]

Projection and rejection operations can determine vector components parallel or perpendicular to each other. Their notation/equations are below. Bars denote a scalar value representing the magnitude of the projection.

     abs{proj_{vec x}vec y} = {vec x cdot vec y} over {abs{vec y}} proj_{vec x}vec y = {vec x cdot vec y} over {vec y cdot vec y}y reject_{vec x}vec y = x-{vec x cdot vec y} over {vec y cdot vec y}y

Unit quaternions were selected to represent the internal state of the IMU. Unlike Euler Angles, which suffer from gimbal lock, they are robust. Also, they are mathematically more efficient and numerically stable than orientation matrices.

q = left[matrix{q_1##q_2##q_3##q_4} right] where {q_1}^2+{q_2}^2+{q_3}^2+{q_4}^2=1

The best way to understand orientation is through their axis-angle representation, where a unit vector, v, “indicates the direction of an axis of rotation” and an angle, theta, “describes the magnitude of the rotation around the axis.” http://en.wikipedia.org/wiki/Axis-angle_representation

q = left[matrix{cos( %theta /2)##v_1sin(%theta/2)##v_2sin(%theta/2)##v_3sin(%theta/2)} right]

The conjugate and multiplication operations are defined below.

x^-1 = [ x_1,-x_2,-x_3,-x_4 ] x * y = left[matrix{x_{1}y_{1}-x_{2}y_{2}-x_{3}y_{3}-x_{4}y_{4}##x_{1}y_{2}+x_{2}y_{1}+x_{3}y_{4}-x_{4}y_{3}##x_{1}y_{3}-x_{2}y_{4}+x_{3}y_{1}+x_{4}y_{2}##x_{1}y_{4}+x_{2}y_{3}-x_{3}y_{2}+x_{4}y_{1}} right]

The derivative of a quaternion, where omega is the rotational rates for each axis, is defined below.

%omega = left[matrix{0 ## %omega_x ## %omega_y ## %omega_z }right] q' = {1} over {2} q * %omega q' = left[matrix{ -{{1} over {2}} q_{2}%omega_{x}-{1 over 2}q_{3}%omega_{y}-{1 over 2}q_{4}%omega_{z}##{1 over 2}q{1}%omega_{x}+{1 over 2} q_{3}%omega_{z}-{1 over 2}q_{4}%omega_{y}##{1 over 2}q_{1}%omega_{y}-{1 over 2}q_{2}%omega_{z}-{1 over 2} q_{4}%omega_{x}##{1 over 2}q_{1}%omega_{z}+{1 over 2}q_{2}%omega_{y}-{1 over 2}q_{3}%omega_{x}} right]

The formula for rotating a vector by a unit quaternion is captured below. To rotate in opposite direction the conjugate of the quaternion is used.

rotate_{vec x}q = q* left[matrix{0##v} right] * q^-1 rotate_{vec x}q = left[matrix{v_{x}(1-2{q_{3}}^{2}-2{q_{4}}^{2})+2v_{y}(q_{2}q_{3}-q_{1}q_{4})+2v_{z}(q_{2}q_{4}+q_{1}q_{3})##2v_{x}(q_{2}q_{3}+q_{1}q_{4 })+v_{y}(1-2{q_{2}}^{2}-2{q_{4}}^{2})+2v_{z}(q_{3}q_{4}-q_{1}q_{2})##2v_{x}(q_{2}q_{4}-q_{1}q_{3})+2v_{y}(q_{3}q_{4}+q_{1}q_{2})+v_{z}(1-{2q_{2}}^{2}-{2q_{3}}^{2})}right]

{rotate^-1}_{vec x}q = q^-1* left[matrix{0##x} right] * q {rotate}^{-1}{vec x}q = left[matrix{v_{x}(1-2{q_{3}}^{2}-2{q_{4}}^{2})+2v_{y}(q_{2}q_{3}+ q_{1}q_{4})+2v_{z}(q_{2}q_{4}-q_{1}q_{3})##2v_{x}(q_{2}q_{3}-q_{1}q_{4 })+v_{y}(1-2{q_{2}}^{2}-2{q_{4}}^{2})+2v_{z}(q_{3}q_{4}+q_{1}q_{2})##2v_{x}(q_{2}q_{4}+q_{1}q_{3})+2v_{y}(q_{3}q_{4}-q_{1}q_{2})+v_{z}(1-{2q_{2}}^{2}-{2q_{3}}^{2})}right]

The rotation that provides the shortest arc between two vectors is captured below. The cross product does not produce valid results when the vectors are parallel. This condition has to be checked prior as part of the algorithm.

rotate_{vec x}vec y = left[matrix{ s over 2 ## {x times v} over s } right] where s = sqrt{2(1+vec x cdot vec y)}

rotate_{vec x}vec y = left[matrix{ s/2 ## (x_2{y_3}-x_3{y_2})/s ## (x_3{y_1}-x_1{y_3})/s ## (x_1{y_2}-x_2{y_1})/s } right] where s = sqrt{2(1+x_1{y_1}+x_2{x_2}+x_3{y_3})}

Another method of estimating the quaternion rotation between two vectors is through an optimization algorithm, which minimizes the error for the objective function below. This was used by Sebastian Madgwick and served as a starting point for the IMU algorithm.

min csub q f ({{rotate}^{-1}}_{vec x}q - vec s) newline

The optimization method used by Sebastian Madgwick was the gradient descent algorithm (see below). It was selected due to its efficiency and simplicity. J is the Jacobian matrix of function, f().

vec y = vec x - %mu left ( {nabla f} over abs{ nabla f } right ) Where nabla f = J_{f}f( )

Full expanded, the function to be minimized is depicted below. This formula was originally derived in Sebastian's paper.

f() = left[matrix{v_{x}(1-2{q_{3}}^{2}-2{q_{4}}^{2})+2v_{y}(q_{2}q_{3}+q_{1}q_{4})+2v_{z}(q_{2}q_{4}-q_{1}q_{3})-s_{x}##2v_{x}(q_{2}q_{3}-q_{1}q_{4 })+v_{y}(1-2{q_{2}}^{2}-2{q_{4}}^{2})+2v_{z}(q_{3}q_{4}+q_{1}q_{2})-s_{y}##2v_{x}(q_{2}q_{4}+q_{1}q_{3})+2v_{y}(q_{3}q_{4}-q_{1}q_{2})+v_{z}(1-{2q_{2}}^{2}-{2q_{3}}^{2})-s_{z}}right]

The Jacobian for objective function is:

J_f = left[matrix {2v_y{q_4}-2v_z{q_3}#2v_y{q_3}+2v_z{q_4}#-4v_x{q_3}+2v_y{q_2}-2v_z{q_1}#-4v_x{q_4}+2v_y{q_1}+2v_z{q_2}##-2v_x{q_4}+2v_z{q_2}#2v_x{q_3}-4v_y{q_2}+2v_z{q_1}#2v_x{q_2}+2v_z{q_4}#-2v_x{q_1}-4v_y{q_4}+2v_z{q_3}##2v_x{q_3}-2v_y{q_2}#2v_x{q_4}-2v_y{q_1}-4v_z{q_2}#2v_x{q_1}+2v_y{q_4}-4v_z{q_3}#2x_x{q_2}+2d_y{q_3}} right]

For the accelerometer, the vector under rotation v, is the acceleration opposing gravity and should point upward. This can be represented by setting its value and making the optimizations captured below.

v = left[matrix{0 ## 0 ## 1 }right] f() = left[matrix{2(q_{2}q_{4}-q_{1}q_{3})-s_{x}##2(q_{3}q_{4}+q_{1}q_{2})-s_{y}##1-{2q_{2}}^{2}-{2q_{3}}^{2}-s_{z}}right] J_f = left[matrix {-2{q_3}#2{q_4}#-2{q_1}#2{q_2}## 2{q_2}#2{q_1}#2{q_4}#2{q_3}##0#-4{q_2}#-4{q_3}#0} right]

For the magnetometer, the vector under rotation v, points towards magnetic north and has a component that points forward and another pointing downward. The angle between the “north” and “down” parts is a function of location (the angle increases as one travels between the north and south pole). The objective function and its Jacobian for the magnetometer can be seen below.

v = left[matrix{v_x ## 0 ## v_z }right] f() = left[matrix{v_{x}(1-2{q_{3}}^{2}-2{q_{4}}^{2})+2v_{z}(q_{2}q_{4}-q_{1}q_{3})-s_{x}##2v_{x}(q_{2}q_{3}-q_{1}q_{4 })+2v_{z}(q_{3}q_{4}+q_{1}q_{2})-s_{y}##2v_{x}(q_{2}q_{4}+q_{1}q_{3})+v_{z}(1-{2q_{2}}^{2}-{2q_{3}}^{2})-s_{z}}right]

J_f = left[matrix {-2v_z{q_3}#2v_z{q_4}#-4v_x{q_3}-2v_z{q_1}#-4v_x{q_4}+2v_z{q_2}##-2v_x{q_4}+2v_z{q_2}#2v_x{q_3}+2v_z{q_1}#2v_x{q_2}+2v_z{q_4}#-2v_x{q_1}+2v_z{q_3}##2v_x{q_3}#2v_x{q_4}-4v_z{q_2}#2v_x{q_1}-4v_z{q_3}#2x_x{q_2}} right]

Although quaternions were selected to represent the IMU state, some operations are easier to perform using other methods. Rotation matrices are used to specify a reference axis-set. Rotation matrices are orthogonal square matrices, whose determine is zero. Rotation matrices will be denoted by a capital letter.

R = left[matrix{R_{1,1}#R_{1,2}#R_{1,3}##R_{2,1}#R_{2,2}#R_{2,3}##R_{3,1}#R_{3,2}#R_{3,3}} right]

The best way to interpret rotation matrices is through three direction vectors, each specifying an axis of a local coordinate system.

R = left[matrix{vec x# vec y# vec z} right] R = left[matrix{x_1#y_1#z_1##x_2#y_2#z_2##x_3#y_3#z_3} right]

To rotate a vector using a rotation matrix, the vector is multiplied by the matrix as shown below

rotate_{vec x}R = R * x rotate_{vec x}R = left[matrix{{x_1}R_{1,1}+{x_2}R_{1,2}+{x_3}R_{1,3}##{x_1}R_{2,1}+{x_2}R_{2,2}+{x_3}R_{2,3}##{x_1}R_{3,1}+{x_2}R_{3,2}+{x_3}R_{3,3}} right]

To convert from a rotation matrix into a quaternion, the following equation should be used:

q_R = left[ matrix{{n}over4##{R_{3,2}-R_{2,3}}over{n}##{R_{1,3}-R_{3,1}}over{n}##{R_{2,1}-R_{1,2}}over{n}} right] where n = 2sqrt(1+R_{1,1}+R_{2,2}+R_{3,3}) if R_{1,1} + R_{2,2}+R_{3,3}>0

q_R = left[ matrix{{R_{3,2}-R_{2,3}}over{n}##{n}over4##{R_{1,2}-R_{2,1}}over{n}##{R_{1,3}-R_{3,1}}over{n}} right] where n = 2sqrt(1+R_{1,1}-R_{2,2}-R_{3,3}) else if R_{1,1} > R_{2,2} & R_{1,1} > R_{2,2}

q_R = left[ matrix{{R_{1,3}-R_{3,1}}over{n}##{R_{1,2}-R_{2,1}}over{n}##{n}over4##{R_{2,3}-R_{3,2}}over{n}} right] where n = 2sqrt(1+R_{2,2}-R_{1,1}-R_{3,3}) else if R_{2,2}>R_{3,3}

q_R = left[ matrix{{R_{2,1}-R_{1,2}}over{n}##{R_{1,3}-R_{3,1}}over{n}##{R_{2,3}-R_{3,2}}over{n}##{n}over4} right] where n = 2sqrt(1+R_{3,3}-R_{1,1}-R_{2,2}) else

Inputs and Outputs

There are three IMU sensor inputs, each represented by a three-dimensional (3D) vector: gyroscope (g), accelerometer (a), and magnetometer (m). The accelerometer measure acceleration and can be broken into two components, the gravity component, which opposes the force of gravity (points upward), and the motion component, which represents device acceleration relative to the earth. The magnetometer points to the magnetic north pole. Since the direction of the magnetic pole is not orthogonal to the grown plane, i.e. does not form a 90 degree angle with the accelerometer gravity component, it can also be decomposed into two components, the forward component which is the projection of the vector onto the ground plane, and the downward component, which is perpendicular to the ground plane. The gyroscope measure rates relative to three axis of the device, an input for calculating the quaternion derivative (see previous section). This is summarized in the equations below.

vec a = vec a_g + vec a_m vec m = vec m_f + vec m_d vec g = left[matrix{%omega_x ## %omega_y ## %omega_z }right]

The primary responsibility of the IMU is to estimate the orientation, which is internally represented as a quaternion, and acceleration, relative to the ground plane. The gyroscope rates is used to update the orientation while the accelerometer gravity component and the magnetometer forward component is used to dead-reckon the estimate. Acceleration, relative to the ground plane, is derived from removing orientation information from the accelerometer input. This estimate is significantly more noisy than the orientation estimate due to lack of sensor redundancy, and noise from the orientation is included in this calculating.

To perform analytics, it is preferable to report orientation using an intuitive angle-space representation. The most common representation is Euler angles, i.e. yaw, pitch, and roll. These angles represent three rotations (order is important) to constitute one transform. To convert quaternions into Euler Angles, the following formulas can be used. These three values will constitute the orientation output.

yaw = atan2( 2(q_2{q_3}+q_4{q_1}), q_2-q_3-q_4+q_1)
pitch = asin(-2(q_2{q_4}-q_3{q_1}))
roll = atan2( 2(q_3{q_4}+q_2{q_1}), -q_2-q_3+q_4+q_1)

Definitions

Normalize Quaternions
  [1, 0, 0, 0]	no rotation
  [0, 1, 0, 0]	180deg turn around X axis
  [0, 0, 1, 0]	180deg turn around Y axis
  [0, 0, 0, 1]	180deg turn around Z axis
  [sqrt(0.5), sqrt(0.5), 0, 0]	90deg turn around X axis
  [sqrt(0.5), 0, sqrt(0.5), 0]	90deg turn around Y axis
  [sqrt(0.5), 0, 0, sqrt(0.5)]	90deg turn around Z axis
  [sqrt(0.5), -sqrt(0.5), 0, 0]	-90deg turn around X axis
  [sqrt(0.5), 0, -sqrt(0.5), 0]	-90deg turn around Y axis
  [sqrt(0.5), 0, 0, -sqrt(0.5)]	-90deg turn around Z axis

Gyroscope Equations
(dot q) lsub{E} lsup{S} <- current orientation
(dot q) lsub{E} lsup{S} = [ dot q_{1}, dot q_{2}, dot q_{3}, dot q_{4} ]
(hat q) lsub{E} lsup{S} <- previous orientation
(hat q) lsub{E} lsup{S} = [ q_{1}, q_{2}, q_{3}, q_{4} ]
s_{ %omega } <- gyroscope rates
s_{ %omega } = [ 0, %omega_{x}, %omega_{y}, %omega_{z} ]
(dot q) lsub{E} lsup{S} = {1} over {2} cdot (hat q) lsub{E} lsup{S} times s_{ %omega }
(dot q)_{%omega,t} lsub{E} lsup{S} = {1} over {2} cdot (hat q)_{est,t-1} lsub{E} lsup{S} times s_{ %omega_{t} }
(dot q)_{%omega,t} lsub{E} lsup{S} = left[matrix{ -{{1} over {2}} q_{2}%omega_{x}-{1 over 2}q_{3}%omega_{y}-{1 over 2}q_{4}%omega_{z}##{1 over 2}q{1}%omega_{x}+{1 over 2} q_{3}%omega_{z}-{1 over 2}q_{4}%omega_{y}##{1 over 2}q_{1}%omega_{y}-{1 over 2}q_{2}%omega_{z}-{1 over 2} q_{4}%omega_{x}##{1 over 2}q_{1}%omega_{z}+{1 over 2}q_{2}%omega_{y}-{1 over 2}q_{3}%omega_{x}} right]
(q)_{%omega,t} lsub{E} lsup{S} = (hat q)_{%omega,t-1} lsub{E} lsup{S} + (dot q)_{%omega,t} lsub{E} lsup{S} %DELTA t

General Optimization Algorithm
J^{T} <- Jacobian
E_{hat d} <- reference direction
E_{hat d} = [ 0, d_{x}, d_{y}, d_{z} ]
s_{hat s} <- measured direction
s_{hat s} = [ 0, s_{x}, s_{y}, s_{z} ]
min csub{(hat q)_{%omega,t} lsub{E} lsup{S}} f( (hat q)_{%omega,t} lsub{E} lsup{S}, E_{hat d}, s_{hat s} )
f( (hat q)_{%omega,t} lsub{E} lsup{S}, E_{hat d}, s_{hat s} ) = (bar hat q)_{%omega,t} lsub{E} lsup{S} times E_{ d} times (hat q)_{%omega,t} lsub{E} lsup{S} - s_{ hat s }
(dot q) lsub{E} lsup{S} = (hat q) lsub{E} lsup{S} - %mu { nabla f((hat q)_{k} lsub{E} lsup{S}, E_{hat d}, s_{hat s})} over { ldline nabla f((hat q)_{k} lsub{E} lsup{S}, E_{hat d}, s_{hat s}) rdline }
nabla f((hat q)_{k} lsub{E} lsup{S}, E_{hat d}, s_{hat s}) = J^{T}((hat q)_{k} lsub{E} lsup{S}, E_{hat d}) f((hat q)_{k} lsub{E} lsup{S}, E_{hat d}, s_{hat s})